## Slide 1
⚡ 36-HOUR HACKATHON
IDEATION ROUND
DroneTrackAI
Real-Time Object Tracking Drone using Computer Vision & ROS 2
Team: Team NOS | Track: Robotics & AI | April 2026
Simulation
ROS 2 + Gazebo
YOLOv8
Detection
Kalman Filter
Tracking
PID Control
3-Axis Loops

## Slide 2
Problem Statement
The Core Challenge
Modern surveillance, search-and-rescue, and security operations demand autonomous aerial tracking. Human operators cannot react fast enough or maintain continuous lock on moving targets:
Manual drone piloting loses target in complex environments
Latency in human reaction creates tracking gaps
No robust real-time feedback loop between vision and flight control
Existing solutions lack integration of detection + estimation + control
70%
of rescue missions involve moving targets (FEMA 2023)
3–5×
slower response with manual drone piloting vs. autonomous
< 50ms
required detection latency for stable tracking

## Slide 3
Objective
What We Aim To Achieve
🎯 Real-Time Object Detection
Simulate YOLOv8-class detection on moving targets (person/vehicle) with normalized bounding box output at >30 FPS.
📡 Kalman Filter Tracking
Smooth noisy detections and predict target motion using a constant-velocity Kalman filter for robust state estimation.
🚁 PID Control Loops
Three independent PID loops (yaw, altitude, forward) translate tracking errors into stable flight commands in real time.
🔗 ROS 2 Integration
Full topic-based architecture connecting detection → tracking → control → flight bridge, visible in RViz and Gazebo.
📊 Live Monitoring & Tuning
rqt_plot dashboards and live parameter tuning via ros2 param without restarting nodes.
🔌 Hardware-Ready Architecture
Plug-in MAVROS bridge to deploy identical logic on real PX4/ArduPilot hardware with minimal code changes.

## Slide 4
Proposed Solution
DroneTrackAI — One Pipeline. Zero Tracking Gaps.
🛰️ Simulated YOLOv8 Detection
detection_node.py mimics a camera + YOLOv8 model, publishing normalized bbox centroids and area to /detection/bbox at configurable FPS. Drop-in swap for real YOLOv8 with 4 lines of code.
📈 Kalman Filter State Estimator
tracker_node.py absorbs noisy bbox data and outputs smooth /track/state + /track/velocity. Handles target occlusion with prediction-only mode for up to N missed frames.
⚙️ Triple-Axis PID Controller
pid_controller_node.py runs three decoupled loops: yaw (horizontal centering), altitude (size/area control), forward (distance keeping). All gains tunable live.
🚀 Flight Bridge + Gazebo Physics
flight_bridge_node.py integrates velocity commands and publishes /drone/pose feedback. Full Gazebo world with walking actor; swap to MAVROS for real flight.

## Slide 5
Tech Stack
Robotics
ROS 2 Humble
Gazebo Classic
RViz2
rqt_plot
colcon build
Computer Vision
YOLOv8 (sim)
OpenCV
cv_bridge
NumPy
Kalman Filter
Control
PID Controller
3-Axis Loops
Anti-Windup
Live ros2 param
MAVROS bridge
Infra & Comms
geometry_msgs
visualization_msgs
tf2_ros
ros2 bag
Ubuntu 22.04

## Slide 6
Methodology
01
📋
Requirement Sprint
(0–4 hrs)
Problem validation, MVP scope, ROS topic design, PID gain strategy.
02
🏗️
ROS Scaffold
(4–10 hrs)
Package setup, node stubs, topic graph, launch file, param YAML.
03
⚙️
Core Dev Build
(10–22 hrs)
Detection node, Kalman tracker, triple PID, flight bridge & Gazebo world.
04
🤖
CV Integration
(22–28 hrs)
Tune detection FPS, Kalman noise matrices, PID gains per axis.
05
🧪
Test & QA
(28–33 hrs)
Simulate target at varying speeds, occlusion scenarios, ros2 bag replay.
06
🚀
Demo Prep
(33–36 hrs)
Polish RViz layout, record fallback video, prepare live walkthrough.
(0–4 hrs)
(10–22 hrs)
(28–33 hrs)

## Slide 7
System Architecture / Flowchart
Camera
/IMU
(Sensor)
►
Detection
Node
YOLOv8 sim
►
Tracker
Node
Kalman KF
►
PID
Controller
3× PID loops
►
Flight
Bridge
Physics sim
►
Gazebo
World
(environment)
/detection/bbox
/track/state
/track/velocity
/drone/cmd_vel
/drone/pose
Outputs
🗺️ Live Incident Map (RViz)
🚁 Responder Alert (/drone/pose)
📲 Target Status (/track/state)
📊 Command Dashboard (rqt_plot)
Flow: Sensor → Detection → Kalman Tracking → PID Control → Flight Bridge → Simulation Output

## Slide 8
USP & Key Benefits
⚡
Real-Time Pipeline
End-to-end latency under 50 ms from detection to velocity command. PID loops running at 30 Hz maintain smooth target lock.
🌐
Works in Sim & Hardware
Identical codebase runs in Gazebo simulation and on real PX4/ArduPilot via a single MAVROS bridge swap.
🤝
Modular ROS 2 Nodes
Each node is independently replaceable — swap in real YOLOv8 in 4 lines, swap tracker algorithm without touching PID.
🔮
Predictive Tracking
Kalman filter predicts target position during occlusion, maintaining control output for configurable missed-frame window.
🎛️
Live PID Tuning
All gains adjustable via ros2 param at runtime. No restart needed — iterate yaw, alt, forward loops in seconds.
🔓
Open & Extensible
Full ROS 2 bag recording, rqt_plot monitoring. Plug in any YOLO model, tracker, or controller without restructuring.

## Slide 9
Innovation & Differentiation
Feature
Existing Drone Systems
DroneTrackAI
Real-time object tracking
❌ Manual operator
✅ Automated CV pipeline
AI-driven detection
❌ Not available
✅ YOLOv8-class sim + plug-in real
State estimation
⚠️ Raw bbox only
✅ Kalman filter with velocity predict
PID flight control
⚠️ Single-axis or manual
✅ Triple-axis decoupled loops
Hardware portability
❌ Platform-locked
✅ MAVROS bridge, any PX4/ArduPilot
Live parameter tuning
⚠️ Restart required
✅ ros2 param at runtime

## Slide 10
Future Scope
Phase 2
(1–3 months)
Real YOLOv8 integration
(ultralytics)
Multi-target tracking
(SORT / DeepSORT)
ROS bag auto-analysis
pipeline
Phase 3
(3–6 months)
Real hardware deployment
(PX4 + MAVROS)
GPS-fused altitude
estimation
Deep learning re-ID
for target swap recovery
Phase 4
(6–12 months)
Swarm coordination
(2+ drones, one target)
Edge inference on
Jetson Nano
Encrypted comms
& remote ops center
🌍 Ultimate Vision: Fully autonomous drone swarms deployed for disaster response, border patrol, and wildlife monitoring globally.

## Slide 11
Our Team
AK
Member 1
Team Lead / ROS Dev
ROS 2, Python, System Design
LinkedIn ↗
PS
Member 2
CV & AI Engineer
YOLOv8, OpenCV, Kalman Filter
LinkedIn ↗
RV
Member 3
Controls Engineer
PID, MAVROS, ArduPilot
LinkedIn ↗
SP
Member 4
Simulation & DevOps
Gazebo, RViz, Docker, colcon
LinkedIn ↗
Building autonomous systems for the physical world — one ROS node at a time. 🚁

## Slide 12
Thank You!
Let's build autonomous systems that protect and serve.
📧 teamNOS@dronetrack.dev
🔗 github.com/team-nos/drone-tracker
🌐 team-nos.vercel.app
🙋 Q&A — We're ready!